Auto-Antenna Control
Design an antenna that tracks UAVs

---
Motor Position System Modelling

---
Windowed Velocity looks promising to fit

---
Given target, can now predict the trajectory of motor pose

---
No open loop control, passing target as is

---
No predictor, max lag ~0.5s

---
With predictor, max lag ~0.2s

---
Given feedback of steps, we observe actual orientation deviates heavily

---
Pose when seen with respect to steps tracked by motor

---
Initialization of elevation angle
Followed by tracking a virtual UAV circular trajectory.
Following slides contains the target and obtained trajectories

---
Motor tracks steps nicely, except when it’s unfeasible (velocity saturates)

---
Overall tracking with respect to steps feedback is nicely tracking

---
Pose Predictor
Pose Predictor
Apart from proper tracking, we observed that pose feedback from UAVs are usually at low rates of 1-4Hz. We built a pose predictor that up-samples the incoming pose stream by fitting a parabola using higher order moments (velocity and acceleration) at that given moment. Upsampling rate is set as a config parameter.
This predictor takes care of the lag introduced by propagation delay of the pose message from the UAV to the predictor, and updates it’s prior afresh every time a new pose message is received.

---
Find the codebase here: GitLab